## Slide 1: The Smith Chart
Dave Glawson – WA6CGR
SBMS – October 6, 2011

## Slide 2: What is it?
Problem Solving Aid for RF
A Graphical Demonstrator of How Many RF Parameters Behave at One or More Frequencies
Problems Solved Manually One Frequency at a Time

## Slide 3: Terms
Impedance (Z0) (R+jX, R-jX)
Admittance (Reciprocal of Impedance) (Y0, =Z-1=1/Z)
Reactance +jX, -jX
Susceptance G+jB, G-jB (Reciprocal of Reactance)
Resistance in Ohms
Conductance in Siemens (Mhos) (Reciprocal of Resistance)
Characteristic Impedance of Z0 = Characteristic Admittance of Y0

## Slide 4: Terms
Characteristic Impedance (Z0) is Normalized
Z0 = 50Ω Has No Special Significance
  For minimum loss Z0 = 77Ω
  For maximum breakdown voltage Z0 = 30Ω
  For minimum temperature rise Z0 = 60Ω
Γ (Gamma) = (ZL-Z0) / (ZL+Z0)

## Slide 5: Impedance Coordinates

## Slide 6: Admittance Coordinates

## Slide 7: Constant SWR Circles

## Slide 8: Effect of Adding Series Reactances or Shunt Susceptances

## Slide 9: Determine the “Q” of Your Amplifier
Select the “Mean” Frequency of Your Band
Divide the “Mean” Frequency by the expected 3dB Bandwidth
Q=Fo/3dB BW
Example Center of Frequency Range = 450 MHz
3 dB Bandwidth of 100 MHz
Q = 450/100 = 4.5

## Slide 10: Smith Chart “Q” Circles

## Slide 11: References
http://www.ham-radio.com/sbms/smithchart
WinSMITH
Example – MRF327