## Slide 1: How To Adapt Satellite Dish Hardware to Monitor Airliner Radar Altimeters
cheap

## Slide 2
3,400 to 4,200 MHz (C-band)

## Slide 3
3,400 to 4,200 MHz (C-band)
You don’t need a dish for ranges less than 4 miles.

## Slide 4
3,400 to 4,200 MHz (C-band)
You don’t need a dish for ranges less than 4 miles.
But you will need these.

## Slide 5
repackage (optional)
needs modification
“Sat Finder”
Horn
LNB
12 V Battery

## Slide 6
http://www.satpro.tv/single-output-c-band-lnb.aspx
http://www.satpro.tv/conical-scalar-ring-c-band-lnb-bracket.aspx
repackage (optional)
http://www.all-battery.com/12v2000mahnimhbatterypack11606.aspx
$23
$10
$16
$16
http://www.ebay.com then keyword: “satellite finder”
needs modification

## Slide 7
http://www.ebay.com then keyword: “satellite finder”
repackage (optional)
You need to disable the low pass filter.
$10
needs modification

## Slide 8
You need to disable the low pass filter.
remove C12
repackage (optional)

## Slide 9
You need to disable the low pass filter.
(Re-packaging optional)
remove C12
repackage (optional)

## Slide 10
remove C12
Close Up View

## Slide 11
Output goes to sound card, or oscilloscope.
The red and black wires that go to the squawker… is your output.
repackage (optional)

## Slide 12
How to Display the Output
Input to your computer's sound card to: Spectran a free spectrum analyzer
http://www.weaksignals.com/
Listen to the output on anything that accepts line level, or watch it on an oscilloscope.

## Slide 13
How to Display the Output
Input to your computer's sound card to: Spectran a free spectrum analyzer
http://www.weaksignals.com/
Listen to the output on anything that accepts line level, or watch it on an oscilloscope.
Spectran allows you to pass the signal through to your computer’s speakers.

## Slide 14
Output Examples
(To play these wave files, they must be in the same folder with this .pptx file.)
 distant means weak. Use the volume control hear it louder.

## Slide 15
Repackaged SatFinder

## Slide 16
Amplifier and SatFinder go up to the WiFi frequency.
Note the amplifier in place of the C-band LNB
Repackaged SatFinder

## Slide 17
950 to 2,400 MHz
Amplifier and SatFinder go up to the WiFi frequency.
Note the amplifier in place of the C-band LNB

## Slide 18
The wi-fi antenna needs an amplifier, the LNB does not.

## Slide 19
This setup will allow you to see the spectrum of the modulation of your neighbor’s WiFi.

## Slide 20
http://www.ebay.com then
keyword: inline satellite amplifier
http://www.ebay.com then
keyword: 2.4GHz 25 DBi Yagi WiFi Antenna
$5
$17

## Slide 21
http://www.ebay.com then
keyword: inline satellite amplifier
http://www.ebay.com then
keyword: 2.4GHz 25 DBi Yagi WiFi Antenna
$5
$17
inline .01µ capacitor

## Slide 22
$5
inline .01µ capacitor
Make it your self with F-connectors or by it on eBay. Use keywords: DC power block

## Slide 23
Just for Fun
http://planefinder.net/
http://www.flightradar24.com/
http://flightaware.com/live/
Use these online flight radar maps to associate a particular spectrum (sound) from your monitor to the specific kind of airplane and airline. There’s at least a dozen different signatures. (...a dozen different manufacturer’s models.)
The direction your dish is pointing will tell you which airplane you are listening too.
Wikipedia on Radar Altimeters
http://en.wikipedia.org/wiki/Radar_altimeter

## Slide 24
Just for Fun
Motorize elevation with a drill motor on standard dish mount.
Azimuth is easy and usually all you need to follow an airplane.
If you don’t have a dish, your range is limited to 2 to 4 miles. (But it’s easier to carry around.)

## Slide 25
Next Project?
How about, monitor the 1092 MHz chatter between airliner and ground
http://www.hamradioscience.com/the-rtl-2832u-sdr-and-ads-b/

## Slide 26
Or…
How about building your own radar altimeter?
http://lea.hamradio.si/~s53mv/radalt/radalt.html